## Slide 1: Network Artificial Intelligence
Connections - 2017
Vinod Kumar S - Huawei

## Slide 2: Network Artificial Intelligence
Telemetry
Telemetry via Streaming
New protocols – gRPC; New technique – Yang Push.
Analytics
Actionable Analytics by SDN, Orchestrator
Messaging Middleware – DDS, Kafka etc
New techniques – In-Situ-OAM
Closed Loop
Real-time mechanism to handle streaming data
Big Data techniques to store telemetry
AI/ML techniques for analysis
Continuous Feedback and improvements
Loose coupling
Networks autonomous through automation and control loops
Use IT tools and techniques - Beam, Flink, InfluxDB etc

## Slide 3: Network Telemetry
What is Telemetry?
Telemetry is an automated communications process by which measurements and other data are collected at remote points and transmitted to receiving equipment for monitoring.
Network Telemetry
Network Telemetry describes how information from various data sources can be collected using a set of automated communication processes and transmitted to one or more receiving equipment for analysis tasks.
Analysis tasks may include event correlation, anomaly detection, performance monitoring, metric calculation, trend analysis, and other related processes.

## Slide 4: Legacy Telemetry
Query based
Trap support
Limited data
Non streaming

## Slide 5: Streaming Telemetry
Streaming
Netconf Restconf YANG
Yang push, gRPC
Publish subscribe

## Slide 6: Bus Based transport option
Feature | Standard socket API | Bus based transport
Architecture | TCP: Point to Point UDP: point to point, broadcast or multicast | Publish-Subscribe (multicast)
Discovery of endpoints | IP addresses, port numbers are hardcoded | Dynamic discovery, no need to specify where end points reside
Device management | Management configuration and Application reachability | Management and configuration is simpler, publish to middleware
Device Publishing | One copy per subscription | Single copy per domain.
VNF / PNF 1
VNF / PNF 2
VNF / PNF 3
Middleware
Subscriber 1
Subscriber 2
Subscriber 3
a
b
c
a
b c
a c

## Slide 7: Protobuf encoding option
VNF / PNF
App
Format
Type consistency
Compatibility
Performance
JSON | XML | Protobuf
human readable | human readable | Dense binary
Easily portable | Easily portable | Need target specific compiler
Self contained | Self contained | Schema dependency
Performance expensive | Performance expensive | Performance optimized
Massive data overhead | Massive data overhead | Optimized metadata overhead

## Slide 8: Streaming Analytics

## Slide 9: Batch / Lambda Architecture
Batch use cases
Write twice
Data duplication
Late events

## Slide 10: Streaming Analytics (Kappa)
Network Streaming Analytics Use cases
Real-time Anomaly detection and action
Network fault handling
BMP: Route leaks / BGP hijack
Congestion avoidance
AI enabled auto bandwidth
Self healing virtualized networks

## Slide 11: Flink streaming framework
Continuous Processing for Unbounded Datasets
accurate, even in case of out-of-order or late-arriving data
stateful and fault-tolerant
Performs at large scale

## Slide 12: Beam programming model
batch and streaming data processing
run on any execution engine
multi language support
unified programming model

## Slide 13: Why a Platform?
Different Telemetry protocols and Mechanism
Realize different use cases quickly by reusing “NTA platform”
Speed and Scale
gRPC, BMP, Syslog etc
Massive scale of network telemetry
Focus on business logic
Hide the internal mechanisms
Ease of adding new telemetry data
Elasticity to scale up or down
Micro-service and container driven architecture

## Slide 14: Architecture
NAI
Collection platform
Network
Collector 1
Collector 2
Collector n
Data
bus
Data bus
Management and Orchestration
Analytics Platform
App 1
App 2
App n
SDN controller
Closed Loop
SBI
Telemetry

## Slide 15: Closed Loop
Networks autonomous through automation and control loops
Actionable Analytics by SDN, Orchestrator
Continuous Feedback and improvements
ML based analytics for prediction
Self healing

## Slide 16: sflow use case
NTA – Network Telemetry & Analytics
SDN
OVS
DDS Sflow
collector
management
DDS
Kafka
Flink
Beam
Traffic Prediction NTA App
Data Persistence
DDS BUS
Rest
Sflow
Sflow
Openflow

## Slide 17: Prediction Snapshot

## Slide 18: Looking forward…
IETF
  Explore the possibility of bus based transport for telemetry
  Evaluate the option of extending the encoding (content type) of telemetry protocols
  gRPC/gNMI under IETF
IRTF
  Work towards the “proposed” NMLRG research group to discuss the analytics and ML in network
Opensource
  Enhance/Reuse network analytics platforms such as DCAE (ONAP), PNDA.
  Work with open source machine learning libraries such as tensor flow for network specific use cases.

## Slide 19: Thank you
Check out the demo during Hackathon tomorrow!