## Slide 1
In-situ OAM @ IETF
November 8, 2017

## Slide 2: How to send OAM information in packet networks?
In-band OAM
  OAM traffic embedded in the data traffic but not part of the payload of the packet
  OAM “effected by data traffic”
  Example: IPv4 route recording
Out-of-band OAM
  OAM traffic is sent as dedicated traffic, independent from the data traffic (“probe traffic”)
  OAM “not effected by data traffic”
  Examples: Ethernet CFM (802.1ag), Ping, Traceroute
“On-Board Unit”
Speed control by police car
Notes:   Note the difference to transport OAM (SDH/SONET):
  In SONET/SDH there is a constant flow of frames
  OAM is a bit-stream/data between the data encoding sublayer and the physical media and present in every frame, but not part of the data payload
  This mode of OAM transport is often referred to as “out of band”, because OAM has it’s own “channel” – but still resides side by side with the payload data (if present)

## Slide 3: In-situ OAM - Motivation
Multipath Forwarding – debug ECMP networks
Service/Path Verification – prove that traffic follows a pre-defined path
Service/Quality Assurance – Prove traffic SLAs, as opposed to probe-traffic SLAs; Overlay/Underlay
Derive Traffic Matrix
Custom/Service Level Telemetry
“Most large ISP's prioritize Speedtest traffic and I would even go as far to say they probably route it faster as well to keep ping times low.”
Source: https://www.reddit.com/r/AskTechnology/comments/2i1nxc/ can_i_trust_my_speedtestnet_results_when_my_isp/

## Slide 4: What if you could collect operational meta-data within your traffic?
Example use-cases...
Path Tracing for ECMP networks
Service/Path Verification
Derive Traffic Matrix
SLA proof: Delay, Jitter, Loss
Custom data: Geo-Location,..
Meta-data required...
Node-ID, ingress i/f, egress i/f
Proof of Transit (random, cumulative)
Node-ID
Sequence numbers, Timestamps
Custom meta-data

## Slide 5: In-Band OAM (iOAM) in a Nutshell
Gather telemetry and OAM information along the path within the data packet, (hence “in-band OAM”) as part of an existing/additional header
  No extra probe-traffic (as with ping, trace, IPSLA)
Transport options
  IPv6: Native v6 HbyH extension header or double-encap
  VXLAN-GPE: Embedded telemetry protocol header
  NSH: Type-2 Meta-Data ... additional encapsulations being considered/WIP (incl. SRv6, IPv4, MPLS)
Deployment
  Domain-ingress, domain-egress, and select devices within a domaininsert/remove/update the extension header
  Information export via IPFIX/Flexible-Netflow/publish into Kafka
  Fast-path implementation
Hdr
OAM
Payload
iOAM domain
Node-ID,..
Ingress/Egress I/F, ..
Timestamp, Delay,..
Proof of Transit
Sequence number
Generic customer data

## Slide 6
IPFIX
1
3
4
5
6
2
A
C
B
D
Payload
Hdr
Payload
Hdr
Payload
Hdr
r=45/c=17
A
1
C
4
Payload
Hdr
r=45/c=39
B
A
6
1
C
4
Insert SCV meta-data
Payload
Hdr
r=45/c=0
A
1
SCV meta-data
Path-tracing data
Update SCV meta-data
Update SCV meta-data
Update SCV meta-data
SCV Verifier

## Slide 7: In-Band OAM: Information carried
Per node scope
  Hop-by-Hop information processing
    Device_Hop_L
    Node_ID
    Ingress Interface ID
    Egress Interface ID
    Time-Stamp
    Application Meta Data
Set of nodes scope
  Hop-by-Hop information processing
    Service Chain Validation (Random, Cumulative)
Edge to Edge scope
  Edge-to-Edge information processing
    Sequence Number

## Slide 8: Tracing Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Opt Data Len | Elements-left | Reserved1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| OAM-Trace-Type | Reserved2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| | |
| Node data List [0] | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ D
| | a
| Node data List [1] | t
| | a
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. . . S
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ p
| | a
| Node data List [n-1] | c
| | e
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| | |
| Node data List [n] | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
Bit 0 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ Hop_Lim ¦ node_id ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 1 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ingress_if_id ¦ egress_if_id ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 2 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ timestamp seconds ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 3 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ timestamp nanoseconds ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 4 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ transit delay ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 5 | 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ application data ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Bit 15 | Long format of data elements

## Slide 9: Proof-of-Transit Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Opt Data Len | POT type = 0 | reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| Random | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ P
| Random(contd) | O
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ T
| Cumulative | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Cumulative (contd) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+

## Slide 10: Edge-to-Edge Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option Type | Opt Data Len | IOAM-E2E-Type | reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| E2E Option data format determined by IOAM-E2E-Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Option Type: 000xxxxxx 8-bit identifier of the type of option.
Opt Data Len: 8-bit unsigned integer. Length of the Option Data field of this option, in octets.
iOAM-E2E-Type: 8-bit identifier of a particular iOAM E2E variant.
0: E2E option data is 64-bit Per Packet Counter (PPC) used to identify packet loss and reordering.
Reserved: 8-bit. (Reserved Octet) Reserved octet for future use.g

## Slide 11: Transport Options – IPv6, VXLAN-GPE, SRv6, NSH...
IPv6: v6 HbyH extension header
VXLAN-GPE: Embedded telemetry protocol header; Combines with NSH etc.
SRv6: In-Band OAM TLV in v6 SR-header SRH (proof-of-transit only)
NSH: Type-2 Meta-Data (proof-of-transit only)
... more to come: MPLS, IPv4,...

## Slide 12: Running Code: Experimental OpenSource Implementation
Open source experimental Implementation
    FD.io/VPP (see fd.io) – encapsulations: IPv6, VXLAN-GPE, NSH
    OpenDaylight Control App (proof of transit / tracing)
Chipset vendors supporting IOAM
Demo Videos: Google+ In-Band OAM group Youtube In-Band OAM channel

## Slide 13: Demos at IETF BnB

## Slide 14
Node A
Node B
Node C Verifier
Node D
Host 1
Host 3
Host 2
VPP
VPP
VPP
VPP
pmacct
Apache Kafka
OpenDaylight – iOAM6/SCV app
Elasticsearch Logstash Kafka
iOAM6: Decap & Verify
iOAM6: Transit
iOAM6: encap
iOAM event control
iOAM visualization
Payload
Hdr
Payload
Hdr
r=45/c=0
A
1
Payload
Hdr
r=45/c=17
A
1
D
3
1
3
4
2
Payload
Hdr
Data Export IPFIX, kafka
Control Telemetry/ OAM data
Path Verified
Visualization & Analytics

## Slide 15: Use-cases
M-anycast Smart service selection – combining SRv6 and in-situ OAM
In-situ OAM based active network probing
VXLAN-GPE Overlay-Underlay Tracing and SLA Check
A
C
D
B
A
A
B
A
B
C
VXLAN-GPE
4
1
2
0
3
S1
S2
S3
C1
Measure transit delays, server loads, choose optimal service for client and steer connection using SRv6
0
1
2
3
4
5
6
Server
UDP probe configured among all edge nodes (0,1,5,6). Server collects summarized probe info from all edge nodes

## Slide 16: What is happening at IETF100?
Data draft adopted in IPPM wg
Transport -00 for NSH, VXLAN-GPE, GENEVE
IETF 100 hackathon
  VPP and p4 implementation interop
  IOAM on barefoot ASIC