## Slide 1: Stream Control Transmission Protocol and Potential Denial-of-Service Attack
V Anil Kumar
CSIR Fourth Paradigm Institute, Bangalore
anil@csir4pi.in
Debabrata Das
International Institute of Information Technology, Bangalore
ddas@iiitb.ac.in
CSIR-4PI

## Slide 2
CSIR-4PI and its Cyber
Security Research
  Robust Protocol Design
  DESACK
Outline
DDoS attacks: Some Trends and Observations
Chart: 
 | 0.9 | 1.2 | 3 | 10 | 17 | 24 | 40 | 49 | 100 | 60 | 60 | 309 | 325
  Feedback Manipulation in SCTP and DoS Flood
SCTP Packet Traces during Attack
Feedback manipulation
Attack Simulation
100 Mbps 0.01ms
100 Mbps 0.01ms
1Mbps 10ms
100Mbps 0.01ms
100Mbps 0.01ms
S1
S3
R1
R2
D1
D2
D3
S2
Mirai Botnet and the
Recent DDoS against Dyn
Feedback Manipulation Attack Experimentations
Feedback Loops in
Transport Protocols
Sender
Receiver

## Slide 3
Mathematical Modelling of Complex systems and data intensive research
Powered through High Performance computing (360 TF centralized supercomputer)
One of our focuses: Cyber Security Research and Observation (CySeRO)
CSIR Fourth Paradigm Institute (CSIR-4PI)

## Slide 4: Cyber Security Research and Observation Platform @CSIR-4PI
A Programmable, Reconfigurable and Observable Test environment
Emulate wide conditions: Topology, BW, latency, Queuing Scheme;
Buffersize, Packet drop, etc
Configuration: 60 nodes; Self-contained DC (UPS; cooling; automatic door opening, CCTV, Water leakage detection etc.)

## Slide 5
Denial-of-Service attacks are arguably the biggest threat that Cyberspace has been facing
Not new to the security community
  Almost as old as the Internet itself
  However, they have undergone rapid and significant changes
    Increase in amplitude and frequency of attacks
    Sophistication in flood generation
    Illusiveness to detection and mitigation techniques
Flooding Denial-of-Service Attacks

## Slide 6
Gaining more Strength
Flood exceeded 1000 Gbps
Most Powerful DDoS Attacks
Chart: Year
| 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0
 | 0.9 | 1.2 | 3 | 10 | 17 | 24 | 40 | 49 | 100 | 60 | 60 | 309 | 325 | 800 | 1200
Source: Arbor Networks and Dyn

## Slide 7
Mirai: One of the largest botnets ever seen:
  Several thousands of compromised hosts/devices
  Mainly IP cameras, home routers, IOT devices etc. running Linux
Exploited for the largest ever seen DDoS attack
  Oct. 21, 2016 from 7 AM onwards
  Multiple occurrence on the same day
  Estimated flood rate of ~ 1.2 Tbps
  DNS lookup request
  Target: Dyn, an Internet and DNS infrastructure service provider
  A Large Scale DDoS Attack: Real Example
Mirai Spread was through TCP port 23, 2323 and 7547

## Slide 8
  Geographical Distribution of TCP Scan (2323) Originators Observed at CSIR-4PI, Bangalore

## Slide 9
  Geographical Distribution of TCP Scan (2323) Originators Observed at CSIR-4PI, Bangalore

## Slide 10
A Conventional Brute-force Flooding DDoS Attack
Very Powerful: Can virtually detach a network from the Internet !
non-responsive
to congestion
responsive
to congestion

## Slide 11
Reliable protocols needs to operate in a closed loop feedback manner:
  TCP: the well-know transport protocol on the Internet
  SCTP: a new entity in transport layer
  MPTCP: An innovative next generation protocol
Sender
Receiver
Forward Path: Data
Reverse Path: ACK, window update, cong. notification
Feedback Operation of Protocols on the Internet
We have millions of such feedback loops in every seconds
Internet is probably one of the biggest manmade closed-loop feedback system
Reliable Data transfer
Flow control
Congestion Control
Duplicate delivery
Notes: Feedback operation of communication protocol is not a new things! However, it has not been highlighted from a security perspective.

## Slide 12
Feedback manipulation is a potential source of vulnerability in feedback protocol
A feedback manipulation attack takes place when the receiver manipulates the feedback with malicious intention
Typically, the manipulation (i.e the manipulated packet) does not violate the protocol standard in both syntax and semantics
  Acceptable to the sender
  But still can impose damage such as DoS to sender or its upstream network
Security Concern in Feedback Protocols

## Slide 13
Is feedback manipulation a potential vulnerability in next generation protocols ?
Can it be exploited to constitute powerful and sophisticated attack scenarios ?
How feasible are such attacks ?
What are the impacts ?
How to design protocols robust to feedback manipulation ?
Feedback Manipulation Attacks
Feedback Manipulation Flooding Denial-of-Service Attacks
Tactical manipulation of protocol feedback for flood generation

## Slide 14
Feedback Manipulation Flooding Attack
Conventional Flooding DoS Attack
Feedback Manipulation Flooding Attack
Attacker
Transport
Protocol
A different flooding strategy than being practiced today
* Reverse flood direction; * High flood amplification; * Control on flood pattern

## Slide 15
A relatively new transport protocol
  Connection oriented, reliable protocol
  Originated from SIGTRAN working group for transporting SS7 (telecom signaling)message over IP
  Evolving as a general purpose protocol
  IETF Standard – 4960 (~150 page spec)
Several unique features, not supported by TCP and UDP
  Multi-homing; Multi-streaming; protection against SYN-flooding; etc.
  Message oriented rather than byte oriented
Stream Control Transmission Protocol (SCTP)

## Slide 16
SCTP is a feedback based protocol
  Flow and congestion control are implemented at the sender side, but are strongly controlled and driven by the receiver feedback
Receiver feedback is communicated through SACK
  A 32 bit advertised receiver window (a_rwnd)
  A 32 bit cumulative TSN (Transmission Sequence No.) acknowledgement
  TSN ACK is used for congestion control, and hence to control data transmission rate
Feedback Manipulation Flooding Attack (FMFA) on SCTP

## Slide 17
Each SACK that acknowledges new data (new TSN ACK):
  Decrements the amount of unacknowledged data (flight_size) by the amount of data acknowledged by the TSN filed of SACK
  Increments the cwnd:
    cwnd = cwnd+1 (in slow-start)
    cwnd = cwnd+1/cwnd (in congestion avoidance)
  Sender sends out new data when cwnd > flight_size till flight_size = cwnd
Each SACK with new TSN ACK will trigger new data packet(s)
  Typically one data packet in CA and two SS
cwnd=cwnd/2 upon detection of a data packet loss
End-to-end Congestion Control: A Feedback Driven Process
cwnd can be inflated beyond the path capacity through feedback manipulation

## Slide 18: Optimistic SACK Spoofing in SCTP (The basic Building Block of FMFA)

## Slide 19
We used a simple topology and ns2 for simulation
  Later did extensive real-world experimentations
100 Mbps 0.01ms
100 Mbps 0.01ms
1Mbps 10ms
100Mbps 0.01ms
100Mbps 0.01ms
S1
S3
R1
R2
D1
D2
D3
S2
S1, S2 and S3: SCTP senders and D1, D2, D3: receivers
R1 and R2 Routers with FIFO and max. buffer 40 pkts
Our simulation captures three important aspects:
  Fairness among flows; router buffer dynamics and cwnd dynamics
  They are best suited to visualize the attack
  Highlights how these parameters are pushed to their extreme cases during the attack
Simulation

## Slide 20
Simulation of Normal Scenario
100 Mbps 0.01ms
100 Mbps 0.01ms
1Mbps 10ms
100Mbps 0.01ms
100Mbps 0.01ms
S1
S3
R1
R2
D1
D2
D3
S2
AIMD (Additive increase multiplicative Decrease) of CWND

## Slide 21
Simulation of FMFA
We repeated the previous simulation exactly with one change:
S1-D1 flow is replaced with FMFA flow

## Slide 22
Time in seconds
Data and SACK Chunks
SCTP Sender’s Response to Genuine SACK (Simulation)
During congestion avoidance with delayed ACK
Data
SACK

## Slide 23
Time in seconds
Data and SACK Chunks
SCTP Sender’s Response to Manipulated SACK (Simulation)
Manipulation started here
Data/Flood
SACK (Manipulated)

## Slide 24: SCTP Exploitation: Simulated and Real-world Experimental Result
Experimental Topology SACK Packet Loss and its Impact on Flood-Rate
15 hops real-world
Internet Path

## Slide 25
CWND Comparison during FMFA: Simulation vs. Experimentation
Ns2 Simulation
Linux Kernel: Real-world Experimentation
Slow-start Algorithm
CA Algorithm
Slow-start Algorithm
CA Algorithm

## Slide 26
Can we generate shrew-like flooding pattern through Feedback manipulation ?
Low-rate FMFA

## Slide 27: Low-rate FMFA Simulation
Time (s)
Pkts in Buffer
TSN
Time (s)
Data/Flood
SACK (Manipulated)

## Slide 28
FMFA- the Root Cause
Valid SACK can be generated without seeing/opening the data
We enriched SACK with CPE for making SCTP robust to ACK spoofing: DESACK
Purely Header-driven Acknowledgement: A fundamental limitation

## Slide 29
The most crucial part of the DESACK-enabled SCTP
Designed carefully to make the protocol robust to flood generation through loss-concealment
Robust to data packet reordering, packet loss and duplicate data delivery
Essentially, a binary sum of the 32 bit essence of (PE) of all data being acknowledged through C_TSN_ACK
For a DESACK of C_TSN_A, say, X:
Cumulative Payload Essence (CPE)
Where ISN = Initial Sequence No. PE[i] = Payload Essence of ith packet
CPE is placed in DESACK’s V-tag field and conventional V-Tag validation is replaced with DESACK validation : Static vs. dynamic V-Tag

## Slide 30
Data Enriched SACK Aware SCTP (DESACK-SCTP)
We added three new modules to regular SCTP to obtain DESACK-SCTP
*CPE Generator *DESACK Generator *DESACK Validator

## Slide 31
DESACK: V-Tag Dynamics (Experimental Result)
A 60 second long experiment over the Internet with our DESACK-enabled SCTP

## Slide 32
DESACK: Robustness against Data Packet Loss (Experimental Result)
A 1000 seconds (16+ minutes) long test with varying packet loss
Environment: Combination of controllable testbed and real Internet
Packet loss is introduced at the testbed and the remaining packets are released to the Internet

## Slide 33: Thank You! Questions ?